## Slide 1: Synchrotron Ring Schematic
Bending magnets
B ~ X2
B ~ X
quadrupole magnet
sextupole magnet

## Slide 2: Synchrotrons
Synchrotrons are the most widely used accelerators
  Beam of particles is constrained in a circular path by bending dipole magnets
  Accelerating cavities are placed along the ring
  Charged particles which travel in a circular orbit with relativistic speeds emit synchrotron radiation
Amount of energy radiated per turn is:
here q is the electric charge of a particle, , , and ρ is the radius of the orbit.
For , the energy lost per turn has a numerical value given by:
Some numbers: For large electron positron collider LEP at 86 GeV, . There are about 6∙1012 electrons per beam and hence the power required to make up for this loss . Power needed for RF is about 96 MW.
electron

## Slide 3: Proton and Electron Velocity vs. Kinetic Energy
beam velocity:
total energy:
The relevant formulae are calculated if A1, Z1 and A2, Z2 are the mass number (u) and charge number of the projectile and target nucleus, respectively, and Tlab is the laboratory energy (MeV).
Lorentz contraction factor:
heavy particle (p) become relativistic at higher energies

## Slide 4: Large Electron Positron Collider LEP
For relativistic particles, , hence energy loss grows dramatically with particle mass decreasing, being especially big for electrons. ()
Limits on the amount of the radio-frequency power means that electron synchrotrons (large electron positron collider LEP, used from 1989 until 2000 at CERN) can not produce beams with energies more than 100 GeV.
Notes: (𝑚_𝑝/𝑚_𝑒 )^2=((938 𝑀𝑒𝑉)/(0.511 𝑀𝑒𝑉))^2=3.4∙〖10〗^6

## Slide 5: Electron vs. Proton Machines
Electron Machine | Proton Machine
Clean – no other particle involved than | Messy - or interact and rest of or is junk.
Lower energy for same radius (synchroton radiation). LEP | Higher energy for same radius. LHC () in LEP tunnel
Energy of known | Energy of or not known
Fixed energy (for a given set of operating conditions), | Range of or energies for fixed or energy.
Best for detailed study | Best for discovering new things
Electron Machine | Proton Machine
Fixed energy (for a given set of operating conditions), | 
Best for detailed study | Best for discovering new things
Hadron Collider (note, proton is a complex mixture of quarks and gluons):
Crazy background due to splashed quarks and gluons connected by complex color-charge strings.

## Slide 6: Synchrotrons
The bending field changes with particle beam energy to maintain a constant radius:
B ramps in proportion to the momentum. The revolution frequency also changes with momentum
Maximal momentum is therefore limited by both the maximal available magnetic field B and the size of the ring ρ.
To keep particles well contained inside the beam pipe and to achieve the stable orbit, particles are accelerated in bunches, synchronized with the radio-frequency field.
Analogously to linacs, all particles in a bunch has to move with the circulation frequency in phase with the radio-frequency field.
Requirement of precise synchronization, however, is not very tight: particles behind the radio-frequency phase will receive lower momentum increase, and other way around.
Example: for the large hadron collider LHC (ρ = 2805 [m]) and a magnetic field of the superconducting dipoles is B = 8.33 [T] (Biron = 1.5 [T]) one obtains an energy of Emax = 7 [TeV]
Notes: (𝑚_0∙𝛾∙𝑣^2)/𝜌=𝑞∙𝑣∙𝐵→𝜌=(𝑚_0∙𝛾∙𝑣)/(𝑞∙𝐵)=𝑝/(𝑞∙𝐵) 𝑐∙𝑝=𝛽∙𝐸→1/𝜌=(𝑐∙𝑞∙𝐵)/(𝛽∙𝐸)

## Slide 7: Synchrotrons
Requirement of precise synchronization, however, is not very tight: particles behind the radio-frequency phase will receive lower momentum increase, and other way around.
Therefore all particles in a bunch stay basically on the same orbit, slightly oscillating
To keep particle beams focused, quadrupole and sextuple magnets are also placed along the ring and act like optical lenses

## Slide 8: Synchrotrons
Depending on whether beam is deposited onto a fixed target or is collided with another beam, both linear and cyclic accelerators are subdivided into two types:
“fixed-target” machines
“colliders” (“storage rings” in case of cyclic machines)
Much higher energies for protons comparing to electrons are achieved due to smaller losses caused by synchrotron radiation

## Slide 9: Colliding-Beam Experiment
In a colliding-beam experiment two beams of high-energy particles are made to cross each other.
The total energy of a projectile plus the target particle depends on the reference frame. For the production of high mass particles the relevant frame is given by the “center-of-mass” frame for which the projectile and target have equal and opposite momentum p.
For simplicity let us suppose that the projectile and target particle are the same, or possibly particle-antiparticle (e.g. proton-proton, proton-antiproton, or electron-positron). This means that in this frame both the particles have the same energy, (since we are dealing with relativistic particles, this means kinetic plus rest energy).
In the center-of-mass frame, where the momenta are equal and opposite p1 = -p2, the second term vanishes and we have
i.e. s is the square of the total incoming energy in the center-of-mass frame – this is a quantity that is often used in particle physics.
1 TeV + 1 TeV = 2 TeV available cm energy

## Slide 10: Fixed-Target Experiment
In a fixed-target experiment, a charged particle such as an electron or a proton is accelerated by an electric field and collides with a target, which can be a solid, liquid, or gas.
The total energy of a projectile plus the target particle depends on the reference frame. For the production of high mass particles the relevant frame is given by the “center-of-mass” frame.
For simplicity let us suppose that the projectile and target particle are the same, or possibly particle-antiparticle (e.g. proton-proton, proton-antiproton, or electron-positron). This means that in this frame the particles energies are and (since we are dealing with relativistic particles, this means kinetic plus rest energy.
For one particle we know that and is therefore the same in any frame of reference even though the quantities E and p will be different in the two frames. In the frame in which the target particle is at rest, its energy is and its momentum , so that we have
1 TeV p + fixed target p = 43 GeV available cm energy

## Slide 11: Luminosity Parameters
~ 1011
2808
11 kHz
1034 cm-2s-1
16 μm
10 cm

## Slide 12: Accelerator Complex CERN
Most modern high energy accelerators are a series of linear accelerators and rings.
Each piece is designed to accept and accelerate particles for up to a particular energy.
Transferring a beam of particles between one piece and the next is one of the biggest challenges.

## Slide 13: Accelerator Chains

## Slide 14: The LHC Layout

## Slide 15: Large Hadron Collider (LHC)
LHC (p → ← p) 7(14) TeV
26.7 km circumference
40000 tons of cold mass spread over 27 km
10000 tons of Liquid Nitrogen (at T = 80 K)
60 tons of Liquid Helium (cools ring to final 1.9 K)

## Slide 16: Inside Large Hadron Collider (LHC) Tunnel
1232 superconducting magnets (14.3 m long, B = 0.5-8.33 T, 11700 Ampere)

## Slide 17: High Energy Physics (HEP) - Detectors
A perfect detector should reconstruct any interaction of any type with 100% efficiency and unlimited resolution (get “4-momenta” of basic physics interaction)
Efficiency: not all particles are detected, some leave the detector without any trace (neutrinos), some escape through not sensitive detector areas (holes, cracks for e.g. water cooling and gas pipes, electronics, mechanics)

## Slide 18: Experiments at LHC

## Slide 19: Particle Identification at ATLAS: Detector System @ Colliders
Notes: A Toroidal LHC ApparatuS

## Slide 20: Particle Identification at CMS: Detector System @ Colliders
Notes: Compact Muon Solenoid

## Slide 21: Multi-Purpose Detectors (LHC 2009 - …)