## Slide 1: Ionization detectors
incoming particle
ionization track
ion/e- pairs
Minimum-ionizing particles (Sauli. IEEE+NSS 2002)
different counting gases:
ionization process: Poisson statistics
detection efficiency ε depends on average number <n> of ion pairs

## Slide 2: Effective ionization energies
Large organic molecules have low-lying excited rotational states
→ excitation without ionization through collisions

## Slide 3: Charge transport in gas
Electric field E = ΔU / Δx separates positive and negative charges
E
charge diffusion in electric field
drift velocity
mean time between collisions
mobility
There is a cycle of acceleration and scattering/ionization etc.
drift(w) and diffusion (D) depend on field strength E and gas pressure ρ
charge diffusion
Notes: Gauss distribution

## Slide 4: Ion mobility
For ions there is an interplay between acceleration and
collisions. Ion mobility is independent of field for a given gas at ρ, T = const.
E. McDaniel and E. Mason; The mobility and diffusion of ions in gases (Wiley 1973)
He
Ne
Ar
E/ρ (V/cm/torr)
w+ ~ 10-2 cm/μs
w- ~ 101 cm/μs
ions
electrons

## Slide 5: Electron mobility
drift velocities of electrons in different gases
drift velocities of electrons in Argon-Methan mixtures
reduced electric field strength [V/cm mm Hg]
pure
In general, the mobility of electrons is not constant, but depend on on their kinetic energy and varies with the electric field strength.

## Slide 6: Amplification counters
single-wire gas counter
gas counters may be operated in different operation modes depending on the applied high voltage.

## Slide 7: Ionization chamber
An ionization chamber is operated at a
voltage which allows full collection of
charges, however below the threshold of
secondary ionization (no amplification).
For a typical field strength 500 V/cm and typical
drift velocities the collection time for 10 cm drift is
about 2 μs for e– and 2 ms for the ions.
Time evolution of the signals for one e- ion pair:
electrons
ions
total charge
planar ionization chamber

## Slide 8: Signal collection
The motion of charges induces an apparent current in the electrodes.
Ion causes the same signal as the electron = same sign, same amplitude, but much slower

## Slide 9: Ionization chamber
no gas gain
charges move in electric field
induced signal is generated during drift of charges
induced current ends when charges reach electrodes
additional ´Frisch grid´:
electrons drift towards Frisch grid and induce a signal but not on the anode.
when electrons pass the Frisch grid, a signal is induced on anode.
the angular dependence of the electrons is removed from anode signal
252Cf source (25k f/s)
T1/2=2.645 y
E = 6.118 and 6.076 MeV
binary fission/-decay = 1/31

## Slide 10: 4π twin ionization chamber for fission fragments
measured quantities:
EH
EL
AH
AL
e- drift time
segmented cathode
ϑ
φ

## Slide 11: Fission fragment mass measurement
mass resolution σ = 3 amu
<108.9 amu>
<143.1 amu>
P. Adrich, diploma thesis (2000)

## Slide 12: Determination of the polar angles
P. Adrich, diploma thesis (2000)
angular resolution | 
ϑ | φ
300 | 4.20
500 | 2.50
700 | 2.30
drift velocity: vdrift = 10 (cm/μs)
range of fragments in methan gas: ℓ(E,A)
distance cathode-anode: d = 3.8cm

## Slide 13: Determination of the azimuthal angles
P. Adrich, diploma thesis (2000)
energy ratios for different emission angles ϑ

## Slide 14: Signal generation in ionization counters
primary ionization in gases: I ≈ 20-30 eV/IP
energy loss Δε: n = nI = ne = Δε / I of primary ion pairs n at x0, t0
force: Fe = -eU0/d = -FI
energy content of capacity C
1)
2)
1) + 2)
w+(t)∙(t-t0)
total signal: electron & ion components

## Slide 15: Time-dependent signal shape
total signal: electron & ion components
Both components measure Δε and
depend on position of primary ion pair
x0 = w-∙(te-t0)
for fast counting use only electron component!
drift velocities (w+ > 0, w- < 0)

## Slide 16: Proportional counter
anode wire: small radius RA ≈ 50 μm or less
voltage U0 ≈ (300-500) V
field at r from the wire
avalanche RI → RA, several mean free paths needed
pulse height mainly due to positive ions (q+)
gas amplification factor (typical 104–106) is constant

## Slide 17: Proportional counter
anode wire: small radius ri ≈ 50 μm or less
voltage U0 ≈ (300-500) V
field at r from the wire
avalanche RI → RA, several mean free paths needed
pulse height mainly due to positive ions (q+)
gas amplification factor (typical 104–106) is constant
-U0
r0
ri

## Slide 18: Proportional counter
The primary produced electrons drift the anode wire and reach the area of high electrical field strength. If a critical field strength is reached, a secondary ionization produces electrons in an avalanche.
pos. ion
electron
primary ionization
secondary ionization
pos. ions drift due to
secondary ionization
time sequence of the signal evolution
cloud chamber

## Slide 19: Proportional counter
target
~ φlab
~ tanϑlab
entrance window
V0 ~ 500 V
p = 5-10 Torr
~ 3 mm gap anode-cathode
delay line
Δtime →
Δt ~ tanϑ
i
i
i
o

## Slide 20: Multi-Wire Proportional Chamber
Georges Charpak
Nobel price 1992
Cathode plate
Wires
Amplifier
A multi-wire proportional chamber detects charged particles and gives positional information on their trajectory.
d = 2 mm
charge signals
time resolution: fast anode signals (trise ~ 0.1 ns)
position resolution: for d = 2 mm σx = 50-300 μm
(weighted with charges)

## Slide 21: Multi-Wire Proportional Chamber

## Slide 22: Time Projection Chamber
Principle: Time Projection Chambers are based on the drift of the charge carriers with constant drift velocity vD
in a homogenous E-field (E = -dU/dz).
typical parameters: E ~ 1 kV/cm, vD ~ 1-4 cm/μs, Δz ~ 200 μm
3-dim. traces: z from the drift time, (x,y) from the segmented anode

## Slide 23: Geiger-Müller counter
The discharge is not any more localized
The number of charge carriers is not any more related to the primary ionization
The gas amplification amounts to 108-1010