## Slide 1: Segmented Detectors
Lecture: Hans-Jürgen Wollersheim
e-mail: h.j.wollersheim@gsi.de

## Slide 2: Challenges of γ-ray spectroscopy efficiency vs resolution
Composite HPGe detectors
in ADD BACK mode
Emission at rest
ΔE=2keV
g ray
Channel No.
Counts(arb. units)

## Slide 3: Challenges of γ-ray spectroscopy efficiency vs resolution
High Mγ
Doppler broadening
Emission in flight
v
Solution
Δө
- Segmentation
- Gamma-ray tracking
- Pulse shape analysis
- Doppler correction
Channel No.
Counts(arb. units)
ө

## Slide 4: γ-ray spectroscopy with 3D position sensitive HPGe detectors
In flight g-ray spectroscopy
Decay g-ray spectroscopy after implantation
HISPEC
DESPEC
Efficiency: 43% (M =1) 28% (M =30)
P/T: 58% (M=1) 49% (M=30)
Angular resolution: ~1º
FWHM (1 MeV, v/c=50%) ~ 6 keV
Advanced GAmma Tracking Array

## Slide 5: γ-ray spectroscopy with 3D position sensitive HPGe detectors
Δ
β = 0.5

Via tracking it becomes possible to determine the incident angle and preserve the good energy resolution.
Energy
Counts
PSA = 5 keV
Segment = 12 keV
Detector = 35 keV
Eγ = 1.3 MeV
In flight g-ray spectroscopy
Decay g-ray spectroscopy after implantation

## Slide 6: γ-ray spectroscopy with 3D position sensitive HPGe detectors
In flight g-ray spectroscopy
Decay g-ray spectroscopy after implantation

Background suppression and P/T can be improved by applying imaging techniques.
S. Tashenov, et al. NIMA 586 (2008) 224-228

## Slide 7: HPGe detector
9 cm
7 cm

## Slide 8: Compton suppressed Germanium detektor
peak-to-total ratio
unsuppressed
P/T~0.15
Compton suppressed
P/T~0.6
Interaction in a Ge crystal:
Photo effect (low γ-ray energy)
Compton scattering (medium γ-ray energy)
Pair production e+e- (high γ-ray energy)

## Slide 9: Compton suppressed Germanium detektor

## Slide 10
Gamma Arrays based on Compton Suppressed Spectrometers
Tracking Arrays based on
Position Sensitive Ge Detectors
ε ~ 50 - 25 %
( Mγ = 1 - Mγ = 30)
ε ~ 10 - 7 %
( Mγ = 1 – Mγ = 30)
GAMMASPHERE
EUROBALL
GRETA
AGATA

## Slide 11: HPGe detector – working principle

## Slide 12: HPGe detector – working principle

## Slide 13: HPGe detector – working principle

## Slide 14: HPGe detector – working principle

## Slide 15: HPGe detector – working principle

## Slide 16: HPGe detector – position sensitivity

## Slide 17: HPGe detector – position sensitivity

## Slide 18: Ingredients of γ-ray tracking
Highly segmented
HPGe detectors
AGATA:
Advanced Gamma Tracking Array
Digital electronics
to record and process segment signals
Pulse Shape Analysis to identify the interaction position coordinates
(x,y,z,E)i
Reconstruction of tracks
e.g. by evaluation of permutations
of interaction points
reconstructed γ-rays

## Slide 19: Method to characterize the pulse shape of HPGe detectors
Determine a data-base of pulse shapes S(x,y,z) which allows one to correlate an arbitrarily measured pulse, with an interaction position inside the detector.
How to do this?
Using PET principle in combination with g-ray imaging techniques !
?

## Slide 20: Doppler effect - Efficiency versus energy resolution
With a source at rest, the intrinsic resolution of the detector can be reached.
Efficiency decreases with the increasing detector-source distance.
With a moving source also the effective energy resolution depends on the detector-source distance (Doppler effect)
Small d Large d
Large W Small W
High e Low e
Poor FWHM Good FWHM

## Slide 21: Doppler effect at relativistic energies
for
Lorentz boost:
beam

## Slide 22: Doppler broadening and position resolution
Position resolution
Angular resolution
Energy resolution
beam
projectile
g ray

## Slide 23: Doppler broadening

## Slide 24: Miniball
- 8 clusters à 3 6-fold segmented crystals
total MINIBALL efficiency ~8% at 1.3 MeV
digital electronics, on-board online pulse shape analysis (PSA) for better position resolution

## Slide 25: EUROBALL versus MINIBALL detectors
70cm
20cm
beam
target

## Slide 26: Advanced GAmma Tracking Array
Signals from 36 segments + core
are measured as a function of time
(γ-ray interaction point)
John Strachan

## Slide 27: AGATA at PreSPEC
preprocessor
computer farm
digitiser
Damian Ralet,
Stephane Pietri
AGATA

## Slide 28: Doppler-shift correction 238U on 197Au at 183 AMeV
66.372 | 79 Au | Kα3 | 0.033
66.991 | 79 Au | Kα2 | 27.5
68.806 | 79 Au | Kα1 | 46.4
77.577 | 79 Au | Kβ3 | 5.57
77.982 | 79 Au | Kβ1 | 10.70
80.130 | 79 Au | Kβ2 | 3.84
cos θγ

## Slide 29: Doppler-shift correction 238U on 197Au at 183 AMeV
93.844 | 92 U | Kα3 | 0.099
94.654 | 92 U | Kα2 | 28.2
98.434 | 92 U | Kα1 | 45.1
110.421 | 92 U | Kβ3 | 5.65
111.298 | 92 U | Kβ1 | 10.70
114.445 | 92 U | Kβ2 | 4.15
cos θγ

## Slide 30: Scattering experiment at relativistic energies
Doppler effect
80Kr → 197Au, 150 AMeV

## Slide 31: Example - Coulomb excitation experiment at IUAC
58Ni beam
112,116Sn target
58Ni → Sn at 175MeV
γ-efficiency = 0.005
accelerator duty factor=100%
beam intensity = 0.5pnA
target thickness = 0.2mg/cm2
pγ-rate (Sn) = 1/s
γ-ray spectrum
Doppler effect depends on and

## Slide 32: Position sensitive proportional counter
target
~ φlab
~ tanϑlab
entrance window
V0 ~ 500 V
p = 5-10 Torr
~ 3 mm gap anode-cathode
delay line
Δtime →
Δt ~ tanϑ
i
i
i
o

## Slide 33: Position sensitive proportional counter
~ tan ϑlab
raw γ-ray spectrum
Δt ~ tanϑlab
Δtime →

## Slide 34: Position sensitive proportional counter
~ tan ϑlab
raw γ-ray spectrum
Doppler-shift corrected
γ-ray spectrum
2+

## Slide 35: Position resolution – Double Sided Silicon Strip Detector (DSSSD)
surface of a Microstrip detector
bonding pads

## Slide 36: Simulation result – electrical field configuration
Thomas.Eichhorn@kit.edu

## Slide 37: Current density
Thomas.Eichhorn@kit.edu
Ionizing particle with 450 angle t = 0 ns
Ionizing particle with 450 angle t = 1 ns
Ionizing particle with 450 angle t = 1.1 ns
Ionizing particle with 450 angle t = 1.3 ns
Ionizing particle with 450 angle t = 1.5 ns
Ionizing particle with 450 angle t = 1.7 ns
Ionizing particle with 450 angle t = 1.9 ns
Ionizing particle with 450 angle t = 2.0 ns
Ionizing particle with 450 angle t = 3.0 ns
Ionizing particle with 450 angle t = 4.0 ns
Ionizing particle with 450 angle t = 5.0 ns
Ionizing particle with 450 angle t = 6.0 ns
Ionizing particle with 450 angle t = 7.0 ns
all electrons are collected