## Slide 1: PHL424: Nuclear fission
Lise Meitner, Otto Hahn

## Slide 2: Discovery of fission and the chain reaction
Enrico Fermi (1901-1954)
Theoretician and experimentalist;
Fermi statistics, weak interaction,
first nuclear reactor
Discovery of the neutron by James Chadwick
( 4He + 9Be → 12C + 1n + γ)
(Nobel prize 1935)
Fermi bombarded different nuclei with moderated
neutrons and discovered the induced radioactivity
(Nobel prize 1938 und emigration)

## Slide 3: Discovery of fission and the chain reaction
Discovery of nuclear fission by Hahn, Meitner, Strassmann using radiochemical methods
to verify the fission product Barium (Nobel price 1944 without L.M.)
Otto Hahn (1879-1968)
Lise Meitner (1878-1968)
(Emigration 1938)
Fritz Strassmann (1902-1980)
1939 Detection of fission neutrons, with the potential of a chain reaction
(Szilard predicted this in 1933)
Start of the Manhatten projekt, initiator Szilard
(1939 letter from Szilard, Einstein, Wigner to Roosevelt)
Fermi builts a nuclear reactor and achieved the first controlled nuclear fission reaction
1945 Atomic bomb (fission of U-235 and Pu-239) dropped on Hiroshima und Nagasaki

## Slide 4: Uranium decay
In a Supernova-explosion, approximately 6 billion years ago, the isotopes Uranium-238 (T1/2 =4.5109 years), Uranium-235 (T1/2 =0.7109 years) and Plutonium-239 (T1/2 =24103 years) have been produced in equal parts.
Today Pu-239 is completely decayed, while from U-235 and U-238 0.3 % and 40 % are left over, respectively. Uranium fuel elements require a U-235 enrichment of at least 3 %.
Good Uranium mining means a content of 0,3 % Uranium in sedimentary rock and it will be mined for $50/kg Uranium, the world reserve amounts to about 10 Mio tons of natural Uranium. In addition, 100 106 tons are estimated in rocks with mining costs of $300/kg. Certain are 4,2 109 tons of natural Uranium in sea water which can be extracted for $500/kg.
Alpha-decay:
Spontaneous fission:
- decay of natural Uranium isotopes
Uranium is a silver white shining, soft heavy metal

## Slide 5: Energy gain for 235U
Mass data: nucleardata.nuclear.lu.se/database/masses/
Mass (1u=931.478MeV/c2):
236.045562u → 88.917633u + 143.922940u + 3.025995u
Energy gain: 166.73MeV
Binding energy [M(A,Z) - Z·M(1H) - N·M(1n)] :
-1790.415MeV → -766.908MeV - 1190.239MeV
Energy gain: 166.73MeV
Mass excess [M(A,Z) - A] :
42.441MeV → -76.725MeV – 71.780MeV + 24.214MeV
Energy gain: 166.73MeV
1g Uranium → fission products 68 Million kJ
Energy balance of - fission

## Slide 6: Spontaneous nuclear fission
Fission fragments are deformed
The surface energy and the Coulomb energy is changed due to the ellipsoidal deformation during the fission process.
By exanimating both energy terms one realizes that nuclei with Z2/A ≥ 51 undergo fission spontaneously.
Fission is caused in heavy nuclei by the increasing Coulomb force between the protons.
R
R/21/3
2·R/21/3

## Slide 7: Spontaneous nuclear fission
Fission barrier:
liquid drop model:
 | Z2/A | ES0 [MeV] | EC0 [MeV] | XS | ΔEF [MeV]
235U | 36.02 | 626.0 | 967.4 | 0.773 | 6.1
238U | 35.56 | 625.9 | 963.3 | 0.770 | 6.4
this ratio plays an enormous role
Cohen, Plasil, Swiatecki, Ann. of Phys. 82 (1974), 557

## Slide 8: Energy barrier for spontaneous fission
For nuclei with Z2/A < 51 one has to add energy ΔEF in order to observe fission. However, fission is still possible due to the tunneling effect.
The probability for tunneling decrease however very rapidly with decreasing values of Z2/A, since the fragments have comparatively large masses.

## Slide 9: Double humped fission barrier
delayed fission
prompt fission
Deformation
Energy
240Pu
t1/2=3.8ns
1.
2.
(axis ratio 2:1)
238U(α,2n)240fPu, Eα=25 MeV
Measurement of conversion electrons
Superdeformation
2:1
Hyperdeformation
3:1
Oblate superdeformation
1:2
Oktupole Y31
Oktupole Y30

## Slide 10: Induced nuclear fission
Neutrons have not to overcome a Coulomb barrier. Therefore, slow neutrons can also induce nuclear fission.
Compound-nucleus: g-u
Qfission= [M (238U) + M(1n) – M(239U) ]·c2 = 4.8 MeV
excitation energy relatively small Qfission < ΔEF = 6.4 MeV
fission is not easily possible
Compound-nucleus: g-g
Qfission= [M (235U) + M(1n) – M(236U) ]·c2 = 6.5 MeV
excitation energy relatively large Qfission > ΔEF = 6.1 MeV
fission is easily possible

## Slide 11: Characteristic properties of nuclear fission

## Slide 12: Characteristic properties of nuclear fission
fission asymmetric  multiple highly excited daughter nuclei

## Slide 13: Characteristic properties of nuclear fission
fission asymmetric  multiple highly excited daughter nuclei

## Slide 14: Induced nuclear fission
Yield of fission products for 235U fission. For different neutron energies one obtains different yields of the fission products.

## Slide 15: Characteristic properties of nuclear fission
1000 different -instable nuclei after fission
long lived -emitter together with 239Pu are called radioactive waste
fission asymmetric  multiple highly excited daughter nuclei
examples:
Neutron excess in the daughters:
 many -instable daughter nuclei (often long living)

## Slide 16: Characteristic properties of nuclear fission
examples:
neutron-energy spectrum  evaporation from a moving source
Maxwell-Boltzmann distribution
k = 8.617·10-5 eV/0K
k·T0 = 0.0253 eV for T0=293.61 0K
Important:
Approximately 99% of all neutrons are
immediately released
Only 1% are delayed emitted within a
time window of 0.05s < t < 60s
→ Controlling a nuclear power plant
fragments highly excited & neutron excess
 prompt ( t < 1016s ) neutron emission

## Slide 17: Characteristic properties of nuclear fission
Delayed neutrons ( t  0,2 s  60 s )
 ~1% of the neutrons are delayed
-decay
t½  time delay

## Slide 18: Characteristic properties of nuclear fission
Energy balance of the -fission
Ysmall 100 MeV  (fission nuclei) 8 MeV
Ylarge 70 MeV  (fission nuclei) 7 MeV
n 5 MeV neutrinos ( ) 12 MeV
 (prompt) 7 MeV total: 210 MeV

## Slide 19: Absorption- and fission cross sections for neutrons
Die bei der Spaltung ausgelösten Neutronen können an einer Reihe unterschiedlicher Reaktionen teilnehmen und für weitere Spaltungen verloren gehen.
Beispiel: (n,γ) Absorptionsreaktion
n + U → U* → U + γ
Für 238U ist der WQ für inelastische Stoßprozesse σ(n,n‘γ) größer als der Spaltquerschnitt σ(n,f). In 238U kann keine Kettenreaktion stattfinden.
Eine Kettenreaktion ist nur mit thermischen Neutronen und Spaltung von 235U möglich: → Abbremsen (Moderation) der Neutronen.
235U(n,γ)
235U(n,f)
235U(n,f)
235U(n,γ)

## Slide 20: Absorption- and fission cross sections for neutrons
The neutrons, created during fission, can participate in different reactions and are hence lost for future fission processes.
example: (n,γ) absorption reaction
n + U → U* → U + γ
For 238U the cross section for inelastic collisions σ(n,n‘γ) is larger than the fission cross section σ(n,f). In 238U a chain reaction can not occur.
A chain reaction can occur only with thermalized neutrons and fission of 235U: → slowing down (moderation) of neutrons.
0.0253 eV
thermisch

## Slide 21: Absorption- and fission cross sections for neutrons
We start with thermalized neutrons,
η is the average number of fission neutrons per thermalized neutron.
For 235U: σf = 584 b and σa = 97 b, <ν>=2.4
For 238U: σf = 0 b and σa = 2.1 b
Effective value of η = 1.3 for natural Uranium is too small for chain reaction.
→ 235U has to be enriched to 3% (η=1.8)
0.0253 eV
thermalized

## Slide 22: Interactions of neutrons with matter
Slowing down of neutrons by elastic nuclear collisions:
no excitation, no capture, no fission
Kinematic of the reaction 
example:
Average energy loss of the neutrons per collision:
m
M
v0
v1
v2

## Slide 23: Thermalisation of neutrons
Moderator | Average collision number for a slowing down from 1,75 MeV to 0.025 eV | Tendency to capture thermalized neutrons in relative units
Hydrogen | 18 | 650
Deuterium | 25 | 1
Beryllium | 86 | 7
Carbon | 114 | 10
Example: water ( H2O ) as moderator  scattering on protons, A  1
Rough estimate of the number of collisions k until thermalisation:

## Slide 24: Further neutron losses
238U-absorption
Reactor poison, e.g. the fission product 135Xe: f ( 235U )  500 b
abs  3 000 000 b
Control rod material ( Cd, B )  controlled neutron-absorption
Reactor fuel: tot( 235U )  f( 235U )

## Slide 25: Steering of the chain reaction
Control rods:
Material with large neutron-absorption: B, Cd, In, Ag
fuel rod
moderator
e.g. water
fuel rod
moderator
e.g. water
control rod
e.g. B4C
controlrod
e.g. B4C

## Slide 26: Energy consumption of humans in Germany
turnover of the body (food → heat) 100 Watt
total consumption on primary energy 5000 Watt
(civilization increases consumption by a factor of 50 !!!)
total consumption on final energy (2005) 3700 Watt
electrical power consumption (with industry) 750 Watt
Private households heating and hot water 1000 Watt
Information in power (Watt) = energy / time (Joule/sec) per head, annual mean

## Slide 27: Chemical energy
Origin of the chemical energy: Change of the covalent bonds between atoms which are the molecular building blocks.
12g Carbon-burning with 32g Oxygen (O2) Thermal energy: 393 kJ ~ 30 kJ/gC
reaction C + O2 → CO2 + 4.1 eV
Thermal energy (Q = m·c·ΔT, c = 4180 JK-1kg-1) :
30 kJ can heat up 1 liter of water by 70 Celcius .
Electrical energy (W = power times time) :
30 kJ can keep a 100 Watt lamp 5 minutes long switched on.
Mechanical energy (W = mass · earth acceleration · height) :
30 kJ lift a mass of 70kg 43 meter high.
Chemical energy is atomic energy in the truest sense of the word.

## Slide 28: Comparison with coal burning
If one burns 1 kg of hard coal one obtains an available energy of 8.14 kWh.
In nuclear fission of 1 kg Uranium one obtains an available energy of 22 700 000 kWh.
Nuclear bond 200 MeV is significant stronger than molecular bond 4.1 eV.
Uranium is as „fuel“ three million times more effective than hard coal.
In fission of 1 kg Uranium we obtain the same energy as if we would burn 2800000 kg of Carbon to 10.2 millions kg of Carbon dioxyd!!!

## Slide 29: Nuclear reactor (functional principle)
Reactor core contains
→ fuel enriched Uranium with ~3% U-235
(comparison: enrichment of bomb: 80% U-235)
→ moderator water under high pressure (150 bar), to
slow down the neutrons (increase of the
fission probability) and for cooling
(fission energy is turns into kinetic energy of
fission products, which heats up the fuel)
→ absorber movable control rods (B, Cd, Gd) to
adjust the absorption of the neutrona, so that
k=1 (critical) to keep up the chain reaction.
A fuel rod and Uranium-oxide pellets, the fuel of most power reactors.

## Slide 30: From the fuel pellet to the reactor core
Fuel in form of fuel elements, ~200 of these, each individual water- moderated and cooled. Each element consists of 20-30 fuel rods, each fuel rod consists of 200 Uranium-oxide pellets size of a pellet:
1 cm in height, 1 cm diameter.
fuel pellets
fuel element
reactor core
fuel rod
free space spring
~ 200 pellets tube made out of zirconium
water
entry
e) view from top
on the reactor core
control rods
fuel elements

## Slide 31: Neutron balance in a reactor
Start:

## Slide 32: Reactor dynamics
neutron lifetime:
thermal reactor: ~ 20 μs
fast reactor: ~ 0.5 μs
multiplication factor (reactivity):
k<1 reactor runs down (will be stopped)
k=1 constant power
k>1 reactor runs up (getting started)
How is a reactor running a stable mode?
Why does a reactor not explode?
assumption: k=1.001
after 1 s: 50000 generations
power multiplication per second:
factor 500
fuel temperature
thermal power
reactivity

## Slide 33: Reactor dynamics
How is a reactor running in a stable mode?
burn-off of nuclear fuel
conversion (“breeding”) due
to neutron bombardment
Examples for the change of reactivity during operation:
0.5% of the neutrons from 235-U are emitted delayed by about 10 s from the fission fragments
k<1: under critical reactor
1<k<1+β: delayed critical reactor
k>1+β: prompt critical reactor
decay of fission material
adding neutron poisons
(e.g. Bor in water, control rods)
change in the moderator-fuel ratio
density change of water (temperature)
bubble formation (pos./ neg. reactivity coefficient)
water losses
reactivity losses due to Doppler broadening
of the reaction cross sections at high
temperatures
factor 500
fuel temperature
thermal power
reactivity

## Slide 34: Reactor dynamics
Examples for the change of reactivity during operation:
Xenon peak: 135Xe is a neutron poison
During operation 135Xe will be continuously
reduced du to neutron bombardment
If one reduces the reactor power there will be
an excess of 135Xe (neutron poison), which
will reduce the reactivity even more and only
after many hours it will vanish.
In Tschnobyl all control rods were removed in order to prevent a complete shut-down of the reactor due to the Xe-peak. Then the power increased so fast that the control rods could not been brought back fast enough. The positive bubble coefficient increased the reactivity in addition. First the explosive ejection of fuel made the reactor under-critical.
factor 500
fuel temperature
thermal power
reactivity

## Slide 36: Energy transfer in a nuclear reactor
release of nuclear binding energy during fission
Transfer into kinetic energy of the fission products
Thermal energy due to slowing down of the fragments (neutrons) in the solid fuel
Use of the thermal energy to heat and evaporate the cooling medium (water)
Water steam will be guided to a turbine
Transformation of the rotational energy of the turbine into electrical energy via a
generator
Supply the electricity into the grid
The waste heat will be given either directly (e.g. into a river) or indirectly (e.g. via a cooling tower to air) to the environment.

## Slide 37: Generating electrical energy in a reactor
( im Prinzip wie bei konventionellen Kraftwerken)
Primärkreislauf (Moderator und Kühlwasser) unter hohem Druck von 150 bar, durch Brennelemente auf Temperatur 3300 C erhitzt, gibt Wärme über Wärmetauscher an Wasser des Sekundärkreislaufs weiter, zur Verdampfung bei 70 bar.
Dampf treibt Turbine, Turbine treibt Stromgenerator.
Bilanz: Spaltenergie wird in Wärme, Wärme in elektrische Energie verwandelt. Wirkungsgrad umso höher je höher die Temperaturdifferenz (daher Druck hoch). Typisch 35%.

## Slide 38: Energy transfer in a hot water reactor

## Slide 39: Energy transfer in a pressure water reactor

## Slide 40: Light water reactor in Chernobyl
Der mit Graphit moderierte Siedewasser-Druckröhrenreaktor von Tschernobyl. (Kann natürliches Uran verwenden) Brennelemente hängen in ca. 1660 Druckröhren in senkrechten Bohrungen im Graphit, 210 Steuer- und Absorberstäbe.

## Slide 41: Decay heat
When a nuclear reactor has been shut down and nuclear fission is not occurring at a large scale, the major source of heat production will be due to the delayed beta decay of these fission products (which originated as fission fragments). For this reason, at the moment of reactor shutdown, decay heat will be about 6.5% of the previous core power if the reactor has had a long and steady power history. About 1 hour after shutdown, the decay heat will be about 1.5% of the previous core power. After a day, the decay heat falls to 0.4%, and after a week it will be only 0.2%. (WIKIPEDIA)
The Plutonium-dioxide pellet is glowing red because of the heat generated by the radioactive decay.

## Slide 42: Decay heat after 11 month of operation
Time after shut-down | Decay heat in percent | Thermal power for 4000 MW before shut-down | Time to heat-up 2500 m³ water from 15 °C to 100 °C
10 Sekunden | 3,72 % | 149 MW | 100 min
1 Minute | 2,54 % | 102 MW | 146 min
1 Stunde | 1,01 % | 40 MW | 6 h
1 Tag | 0,44 % | 18 MW | 14 h
3 Tage | 0,31 % | 13 MW | 20 h
1 Woche | 0,23 % | 9 MW | 26 h
1 Monat | 0,13 % | 5 MW | 49 h
3 Monate | 0,07 % | 3 MW | 89 h
If a reactor is operated for the time T0 [s] with a power of P0, then the decay heat power P at the time t [s] after the shut-down of the reactor

## Slide 43: Storage pool
In case of a leakage or failure of the cooling the water can leak out or evaporate. In this case the stored fuel elements can be excessively heated.
Is water still present in the pool, the Zircaloy of the fuel rods can react with the water steam at ~8000 C. In an exotherm redox reaction Zirconium-oxide and Hydrogen is produced which will create an explosive Knallgas mixture in a short time.
In case of no cooling at all the fuel rods can start burning which will destroy the fuel elements.

## Slide 44: Welt Kernenergie
443 nuclear reactors in 30 countries (Jan. 2006)
~16% of the world energy production (2003)
24 reactors in construction